## Slide 1: System Architecture and Performance
CS 294V
Week 06: Memory architecture and caching

## Slide 2: Cache Design
D-Cache
L1
Cache
L2
I-Cache
L1
Cache
L3
Memory Controller
Notes: Only high-end systems sport an L3 cache. Sometimes, the L3 cache is in a different chip by itself, and sometimes it is mounted with the processor in a multichip module.
The L1 is typically split between data and instructions.

## Slide 3: Cache Organization
An inclusive cache is one that contains a copy of all the data in the lower levels
  L2 cache is typically inclusive
  If the L3 is inclusive, then it contains all the data that exist in L2 (and L1), in addition of a lot of other data
An alternative is to have a non-inclusive cache
  For example: L3 can be a victim cache
Notes: A victim cache stores all the cache lines that are evicted from the L1/L2 combo. The idea is that upon a context switch from process P1 into process P2, the latter will start depopulating the P1 cache lines in favor of bringing the cache lines of P2. At some point though in the future, P1 will be switched back. In this case, having a victim cache will ensure that all the items that belong to P1 can be brought into the cache from a nearby location (on demand, of course. There is no bulk transfer of data from L3 to L2 or L1). The verdict of victim vs. inclusive cache is not clear cut. Proponents of the inclusive L3 cache design point out that the large size of the L3 will make an inclusive cache asymptotically identical to that of a victim structure.

## Slide 4: Cache Structure
The cache line is (generally) the unit of transfer from cache to main memory, or between cache levels
64-byte, 128-byte, 256-byte, … 1024-byte
address
address
address
address
address
address
M
E
V
Notes: The bits that indicate the state of the cache line are: M: Modified, E: Exclusive, V: Valid. If V=1 and E=0, it means that there are other caches on other cores or chips that have a copy of this cache line. These bits play an important role in the execution of cache coherence protocols (see L-07). They also play a role in the replacement algorithm. For instance, a cache line with V=0 (an empty slot) will be most beneficiary as a candidate for replacement. Next would be a cache line with V=1 and M=0, because we will not need to flush this cache line all the way to memory. And so on.
The cache line size has been always a fascinating problem, as there is no definitive answer as to what is the optimal size. A larger cache line will require smaller address tags, fewer fetch operations, and if the principle of locality is respected, more data will be used per a single fetch operation. This can be great for reducing the overhead of the cache structure. But it comes with a price. A large cache line will perform poorly if the code does not show good locality of access. In fact, you are bound to bring into the cache data that may not likely to be used. It also puts more pressure on the bus operation, as we need to bring in a larger amount of data per fetch, and this may need for the bus to be wider, or we will have to split the fetch over more than one memory bus cycle. A large cache line also has the potential of bumping out more lines, which can reduce performance.
Please note: Sometimes a cache line is called “cache block” in some literature.
Please note: An unreasonably large cache line can exacerbate the problem of “False sharing”, please see L-07.
How many bits do we store in the address tag? The bits indicating the offset within the line for a data items are not relevant to the comparisons. Therefore it is better to conserve space, power and time by only storing what is necessary. One may argue if we are really down there in the bit twiddling department. The answer is no. Consider a 44-bit address space with a 64-byte cache line. The 6 bits of the offset are about 14% of the address. Saving this amount in the address tag array will yield 14% less area and power. A good deal to have.

## Slide 5: Direct Mapped
address
address
address
address
address
address
M
E
V
address
Example: 2MB L2 cache
128-byte cache width and
a 44-bit address space
The physical address
stored in the directory
will need 44-7 = 37 bits
to identify the cache line
We have 16K lines
Need 14 bits to identify a
line
44-bits
14-bit hash
7-bit offset
=?
Hit
Miss
=
≠
Notes: You pick the hash bits from the address (all addresses here are physical), The same then you use it as an index into the tag array. The address entry in the tag array are then compared against the 37 uppermost bits in the address. If identical, then a cache hit, otherwise, it is pain. How do you pick the hash bits? Keep in mind that we will likely have code that shows good locality. In this case, we want the cache lines belonging to the same memory page to avoid colliding in the cache among one another. So, we want to ensure that those cache lines do not collide. So the safest bits to pick will be those that are after the offset bits. In contrast, if we pick, say, the most significant bits in the address, chances are that the cache lines belonging to the same page will have the same 14 bits hash, which means all lines belonging to the same page will map to the same cache entry, causing a conflict and replacement galore.
The direct mapped cache will have a larger number of replacement due to evictions caused by collisions on the cache. We opt for this structure for the L1 cache. Why? The L1 cache is small, and is in the critical path of instruction execution. Therefore we woul like a very simple structure and this is achieved by the direct mapped cache. Keep in mind also that because of the higher likelihood of collisions, we separate the instructions from the data in the L1 cache. Why? Because not every instruction triggers a data access from/to memory. But every instruction need to be fetched from memory. So, if collisions start evicting instructions, the performance penalty will be high. Therefore, we just opt for separating the two. Keep in mind also that the instruction cache need not have an elaborate write or write miss policy, as the instruction cache is a read-only cache.

## Slide 6: Set Associative
address
address
address
address
address
address
address
44-bits
12-bit hash
7-bit offset
=?
Example: 2MB L2 cache,
4-way set associative cache,
128-byte cache width and
a 44-bit address space
The physical address
stored in the directory
will need 44-7 = 37 bits
to identify the cache line
We have 4K sets
Need 12 bits to identify a
set
Up to 4 lines from each
set can be present, need
to compare all addresses
in a set
=?
=?
=?
Notes: Note the complexity involved here. We will need to do four comparisons (or n comparisons for n-way set associative). Then, we will have, in the case of a miss, pick

## Slide 7: Fully Associative
address
address
address
address
address
address
address
44-bits
37-bit hash
7-bit offset
=?
=?
=?
=?
=?
=?
=?
=?
=?
Example: 2MB L2 cache
128-byte cache width and
a 44-bit address space
The physical address
stored in the directory
will need 44-7 = 37 bits
to identify the cache line
Any line can be stored
In any address
Need to compare all
items
Notes: You can think of the three varieties of implementing caches as a continuous spectrum. On one end, we strict comparisons to only one entry (direct-mapped), and on the other end, we compare everything. Set associative caches thus are somewhere in the spectrum, closer to direct mapped caches because the size of each set is going to be limited by the practical limits on doing comparisons. The Intel example shown earlier in the discussion about TLBs shows that 8 parallel comparisons are probably a practical limit (or perhaps 16 if one wants to push it). So, set associativity is a cache where full association is limited within the confines of a set. The result is a practical way to approximate the benefits of a fully associative cache, while reducing the negative aspects of direct mapped caches.
A question to ponder: What is the impact of the cache structure on power consumption? Tease your mind!

## Slide 8: Comparison
 | Fully Associative | Set Associative | Direct Mapped
Speed | Fast for very small sizes | < Direct map for same size | Fastest
Potential conflicts | Lowest | In-between | Highest
Complexity | Highest | In-between | Simplest
Replacement policy | Complex | Less complex | Simplest
Power consumption | High | > Direct map for same size | Lowest
Notes: The comparison of course is looking at the cache alternatives from a component standpoint rather a system standpoint. Therefore, one has to always weigh other factors in the system that may make a less efficient solution more desirable.

## Slide 9: The Anatomy of a Memory Operation
Execution Pipeline
Load Store Unit
sto r2, (r1)
TLB
val
addr
tid
addr
tid
paddr
Cache
val
paddr
MMU
A write that hits in the cache
Policy 1: Write back (or write behind)
Notes: Keep in mind: The TLB is tagged with an array of virtual addresses. So TLB: (Tag: Virtual, address: physical). For the caches: (Tag: physical, data are in the line). A TLB in design and structure is a special case of a data cache (called fully associative).
Do we need to flush the cache on a context switch? No. Recall that the cache is organized by physical addresses. Therefore, there is no need to worry about the new process illegally accessing the data that belong to the previous process. The new TLB takes care of this protection. Oh, and yes, the TLB has to be flushed on a context switch, or at least, a thread id can be appended to each entry of the TLB.

## Slide 10: Write Hit with Write Through
Execution Pipeline
Load Store Unit
sto r2, (r1)
TLB
val
addr
tid
addr
tid
paddr
Cache
val
paddr
Memory Controller
Main Memory
val
paddr
val
paddr
A write that hits in the cache
Policy 2
Write through
Notes: Technically speaking, the pipeline need not wait for the written data to reach the memory. It can proceed after issuing the write request. However, if so many of these write requests are issued in a short span of time, they will clog the queues that exist in various parts along the path from the pipeline to main memory, which may give a feedback signal to stall the pipeline in case if new write request could overwhelm the queues in the system.
Write through cache perform poorly nevertheless. They consume more power and bus bandwidth than a “smarter” cache that uses write-back policy.

## Slide 11: Write Miss with Write-Back
Execution Pipeline
Load Store Unit
ld r2, (r1)
TLB
val,
addr
tid
addr
tid
paddr
Cache
val,
paddr
Memory Controller
Main Memory
paddr
paddr
Cache line
Cache line
Notes: Observe the following: Even though we want to write 1, 2, 4 or 8 bytes (typically), the cache line is 32-, 64-byte or larger. Therefore, we need to do a “write-allocate” if we have a write back structure. This means that before the write can proceed, the corresponding cache line has to be brought into the cache so that we can do an update on the subset of the cache line that is to be modified. The alternative to the write-allocate policy is to do a write through of the new data into the cache. This will effectively be converting a write-back cache into a write-through cache.

## Slide 12: Cache hit on Read
Execution Pipeline
Load Store Unit
ld r2, (r1)
TLB
addr
tid
addr
tid
paddr
Cache
paddr
val
val
Notes: Now, things look simple here. But imagine the impact of a TLB miss!

## Slide 13: Cache Miss on Read
Execution Pipeline
Load Store Unit
ld r2, (r1)
TLB
addr
tid
addr
tid
paddr
Cache
paddr
Memory Controller
Main Memory
paddr
paddr
cache line
cache line
val
val
Notes: This is straightforward, but observe how many steps are involved. Note that this is an operation where the pipeline may stall due to a cache miss. There is really no cure for this other than multithreading. The wait can be long with nowadays memory. Now, combine this with a TLB miss: Mayhem!

## Slide 14: Seriously?
No, not really
Complexities
  The cache may not handle many concurrent operations
  The cache may not be alone in holding the data
  Some writes or reads are tentative
  Race conditions may occur
  Upon a cache miss on read, we may have to replace a cache line to make room (ditto for writes)

## Slide 15: Pending Operation Queue
Execution Pipeline
Load Store Unit
ld r2, (r1)
TLB
addr
tid
addr
tid
paddr
Cache
paddr
Memory Controller
Main Memory
paddr
paddr
cache line
cache line
val
val
Showing a read miss
What if there is a write after read on the same cache line?
In other words, can we have concurrency?
Notes: The pending operation queues is somewhere between the pipeline and the load-store unit. Typically, it is counted against the L/S unit. You can now appreciate why the L/S unit takes quite a bit of space on the core!

## Slide 16: Tentative (Uncommitted) Writes Queue
Execution Pipeline
Load Store Unit
ld r2, (r1)
TLB
val
addr
tid
addr
tid
paddr
Cache
val
paddr
Memory Controller
Main Memory
paddr
paddr
cache line
cache line
Showing a write miss
val
addr
tid

## Slide 17: Replacement
Execution Pipeline
Load Store Unit
ld r2, (r1)
TLB
val
addr
tid
addr
tid
paddr
Cache
val
paddr
Memory Controller
Main Memory
victim
addr,
victim
cache
line
cache line
cache line
Showing a write miss with replacement
Keep in mind: Replacement ”victim” can be discarded
directly if it has not been modified
val
addr
tid
victim
addr,
victim
cache
line
paddr
paddr
Notes: Replacement policies: There are the: 1) Optimal policy, where we replace only the line that will be used farthest in the future (impractical, we don’t know the future). 2) Least Recently Used (LRU), which approximates the optimal to some degree, but it would be a pain to implement. 3) FIFO: Which does not appear to have any rational reason and generally does not show any superior cache performance. And 4) Random: The simplest to implement. Of course, you run the risk of picking the hot cache line, which can hurt performance.
Note: The replacement policy is only relevant to set-associative caches. Direct-mapped caches have a very simple replacement policy: EVICT THE ENTRY!!!

## Slide 18: Page Coloring
All addresses that map to the same entry in the cache directory are said to be of the same color
If not careful, a program can be allocated addresses that cluster on a few “colors”
The allocation of pages to a process must be such that they can map uniformly over all “colors”
Notes: If a process is allocated memory from only a few colors, then it is as if someone just reduced the cache size as seen by that process. The reason for this is that number of entries in the cache that are available to that process are limited and less than the full range. Performance will suffer.

## Slide 19: Page Coloring: Example
address
address
address
address
address
address
M
E
V
address
44-bits
14-bit hash
7-bit offset
Example: 2MB L2 cache
128-byte cache width and
a 44-bit address space
The physical address
stored in the directory
will need 44-7 = 37 bits
to identify the cache line
Any line can be stored
In any address
Need to compare all
items
Assume 4K Pages
12-bit offset
9-bit color
Notes: The operating system in this example better keeps 2^9 or 512 queues of free pages, and allocates from these pages to the requesting process in a round-robin fashion. This way, the colors are balanced. Of course, when the available memory starts running low, some of these queues may become empty. Then new allocation become suboptimal. It is not a good idea to run a system with over-committed memory.

## Slide 20: Memory
Row select
Column Select
1-bit output
Notes: Memory chips are usually quoted as a product of the number of bits stored multiplied by the number of bits to be read. For example, a 4Gbx1 is a very popular DRAM chip (circa 2020), and it means that the chip holds 4G bits, and one read or write operation occurs in a unit of one bit. 4Gbx4 and other configurations are possible.
Please note that individual memory chips are often quoted in bits (b) not bytes (B).
Please note that to form a byte of storage, we typically combine 8 xxMbx1bit chips in what is so-called DIMM (Dual inline Memory Module). A picture of a DIMM is shown in the slide.
Please note that often, an additional chip is added to the array to store parity. It is essentially the XOR of all the data on the 8 chips. Parity can detect the case when memory content is corrupted due to cosmic ray or noise due to the surrounding environment. Computers operating at high elevation (in mountainous regions) are more susceptible to memory errors.
Sometimes, in high end systems or mission critical systems, additional chips are added to provide even more protection. A Hamming code of 2 arrangement can detect two simultaneous errors and correct a single bit error.
In practice, cosmic rays are not choosy, and they may hit a multitude of chips simultaneously, causing an catastrophic error. We call these transient errors.
In practice, either transient errors are detected, in which case the operating system typically issues a “panic” message and shuts down, or, the transient error is not detected, in which case we have a “silent error”. A silent error may hit a region of memory that we are not using, or that we will overwrite soon. This is the lucky case. The unlucky case if the transient error can lead to a corruption of data, which cannot be recovered easily (if at all detected).

## Slide 21: Memory Controller
Talks directly to the main memory modules
Runs the memory bus protocol
A bus can be a split-transaction
Encodes the addressing of the memory chips in the wires to the memory modules
Notes: The memory controller is responsible for running the memory bus transactions. The transactions can be atomic or can be split transactions. An atomic transaction does not relinquish the bus until it completes. A split transaction allows more performance by splitting the transactions into subtransactions that each runs atomically. Split transactions can be complicated to implement. Bus protocols are very difficult to implement and verify. You will find that in the industry, the memory bus technology changes very slowly in terms of design, although it benefits from increasing bus width and frequency. The complications of designing a new bus are a barrier to designing new protocols, changing the protocol typically requires changing all the devices that connect to the bus, which is a very costly operation.

## Slide 22: Memory Architecture
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Two-socket system with
2 4-core processors
A memory bus connects
all processors
What are the issues?
Notes: The broadcast bus is the simplest form of connections. The earliest shared memory multiprocessors that kept the memory consistent among processors were all implemented on a broadcast bus technology. All participants got to listen to all transactions, which simplified implementations of cache protocols for instance. It also allowed synchronization by locking the bus, in addition to enabling processors to talk to more than one entity at a time. Buses do not have the complication of more sophisticated structures that require complex routing. The problem of the bus structure is both in performance and in physics. In performance, the bus bandwidth is shared among all participants, which means each one of them gets a decreasing share as we add more participants on the bus. In physics, there is only so much length that a bus can have before signal attenuation will make it impractical to operate. This limts the scalability of the bus structure to a typically a handful of processors, certainly no more than a dozen if good performance is to be obtained.

## Slide 23: NUMA: Non-Uniform Memory Architecture
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Memory
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Interconnect
Memory
Memory
Notes: The NUMA structure is a huge deviation from the abstraction of the RAM (Random Access Machine) model upon which all the known algorithm and theory were developed. When we write a program, we assume that all data are equally accessible with the same performance. NUMA systems violate this maxim depending on how memory is allocated to a process. Operating systems go through some pain to allocate memory to processes such that all come from the same node. Then, it follows by scheduling these processes on the chips closest to where the memory is. Generally, writing code in NUMA systems with performance predictability is difficult.
Please note: Elnozahy et al argued in early 2000’s in a paper that the proper way to use NUMA systems is to consider each chip with its own memory as an independent unit, and use message passing between the nodes at the program level. Then, the shared memory is used to speed the performance of message passing. They showed that systems used this way can have superior performance to systems that expose the memory to the programmer.
Please note: NUMA systems are often quoted as a ratio: Like a 1:2 NUMA. This means that this is a system where the remote memory is twice as far in the number of cycles than the local memory.

## Slide 24: NUMA Issues
Memory allocation policies
Process scheduling
Cache affinity
Performance stability
Notes: See the commentary on the previous slide.

## Slide 25: New Concept: Memory Interleaving
If reads and writes are done in the unit of a cache line, then reading and writing bytes is silly
Memory is interleaved to enable parallelism in memory access
bytes mod 0
bytes mod 1
bytes mod 2
bytes mod 3
Notes: Memory interleaving means that the addressing of memory is such that consecutive bytes are spread over several modules (DIMMs), instead of coming from the same DIMM. This way, if we want to read a cache line, we can have parallelism in getting a multitude of bytes instead of pulling one byte at a time.

## Slide 26: New Concept: High Bandwidth Memory
A chip stacked on top of the CPU chip with many connectors, creating a high path to main memory.
HBM is now found in very high-end systems
Several chips can be used depending on cooling arrangement and connections
Can be a massive performance boost
Notes: High bandwidth memory (HBM) is starting to show in modern, high end systems. It is memory that is stacked on top of the processor chip. This solves the limitations on the number of pins. The package is more powerful because HBM is closer to the cores both in terms of lower latency and high bandwidth.

## Slide 27: What to do with HBM?
An L3 cache?
A special area under programmer control?
As part of the address space?
Notes: HBM can be an extension of the caching systems, providing a very large L3 cache. In this way, no programmer or operating system intelligence is needed to benefit from HBM. Alternatively, they can be given to the programmer as a scratch pad. This is akin to very early systems that used an address mode called page-0-addressing. This complicates software, makes it non-portable, and makes virtualization and context switching either expensive or impossible. A third option is to consider HBM as part of the address space and give the operating system control over how to allocate these pages. The theory behind this technique is that the operating system can intelligently use this precious memory to give priority to certain processes, or store performance-sensitive information like page table or kernel data structures. However the modifications necessary for the operating system to perform these functions competently are far from straightforward.

## Slide 28: New Concept: Persistent Memory
Flash memory that can be byte-addressable
  Can read almost the same as speed of DRAM
  Writes can be trickier (also, slow)
Most systems are designed around the notion that memory can lose its content when turned off
Argument is that these can now be fronted by L1—L2—L3 which will mitigate all the bad effects and produce good performance
Can revolutionize the design of operating systems
Notes: Persistent memory allows byte-level access to data in memory and can be used with load and store instructions. This is unlike flash storage devices which are accessed in the size of a disk block. Writes still are expensive because they need to burn material to leave an imprint that cannot be forgotten. This makes these devices great for reading. It is intended that good sized caches can absorb most writes so that the write challenges of this technology does not impact performance badly.