## Slide 1: System Architecture and Performance
CS 258
Week 10: Synchronization Support

## Slide 2: Synchronization Problem Revisited
a++  ld r1, #a
ld r2, (r1)
addi, r2, 1
sto (r1), r2
In principle, an operation that is logically atomic at source level is divided into more than one instructions at the hardware level.
If variable ”a” is shared between two threads, and both execute the instruction then “a++” can result a+1 or a+2
Shared variables must be protected to ensure proper behavior

## Slide 3: Standard Solution: Locking
Mutex m;
m.Acquire
a++
m.release

m.acquire
ld r1, #a
ld r2, (r1)
addi, r2, 1
sto (r1), r2
m.release
But wait! There is no instruction called m.acquire or
m.release
lock and unlock are equivalent to m.acquire and
m.release

## Slide 4: Issues with Locking
Mutex m;
m.Acquire
a++
m.release
Issues with locking
The locking is advisory
The lock implementation
  Spin locks
  Blocking locks
  Wait-free synchronization
Scalability
Performance

## Slide 5: Hardware Support
Test and Set Instruction
tstst (r0)
is equivalent to:
if((r0) == 0) else
set z flag to 1 set z flag to 0
set (r0) to 1
In a single instruction
Hardware ensures atomicity and exclusive access to (r0)

## Slide 6: Simple Implementation of a Spinlock
L1: tstst r0
jnz L1
L1: tstst r0
jnz L1
ld r1, #a
Ld r2, (r1)
addi, r2, 1
sto (r1), r2
clr r0

## Slide 7: Implementing test and set
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
The test and set
instruction requires a lock
on the cache line:
Invalidations from other
caches are denied until
the instruction completes
Question: What are the
requirements?
scalability implications?
multithreading issues?
directory-based vs buses?
Notes: The limits on scalability of bus-based systems have been recognized early in the history of multiprocessor systems. Today, buses are limited only to on-chip interconnect structures (and even these are being challenged). Performance declines with increasing the number of nodes.

## Slide 8: Atomic Actions
atomic {
a++;
}
From C++23 proposal
What is good?
Not advisory, the data access is protected by the word atomic as a single programming unit
Higher level, does not require programmer to think about lock management

## Slide 9: Implementation: Transactional Memory
Add two instructions to signify the start and end of the atomic region
On read or write
  If cache line is locked by transaction, continue.
  If cache line is available but unlocked by transaction, then invalidate cache line, and lock it
  If cache line is not available, send an invalidate request and acquire the cache line in exclusive mode
If a cache line is locked, an invalidate or share request will abort the atomic action
If a cache line is locked, no replacement is allowed
Upon commit:
  All locked cache lines are reset
Upon abort:
  All locked cache lines are reset and invalidated (no write back).

## Slide 10: Limitations on Snooping: What if no Bus?
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Memory
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Interconnect
Memory
Memory
This is not a bus
Notes: Moving to NUMA (Non Uniform Memory Architecture) was recognized early on. Other structures replaced the bus. Examples of such interconnect structures include:
Cross-bar, essentially acting as a n x n connection, or a complete graph, allowing point-to-point communications between any pair in the system. Fast, flexible, power-hungry and expensive. Does not scale well.
Ring, essentially allowing two direct links to each participant, and use forwarding to communicate. Slow, cumbersome, power-efficient and cheap. Scales poorly in performance but allows you keep adding nodes.
A switch, allowing flexibility but routing and contention become issues. Fast, cumbersome, power hungry and expensive. Best in terms of scalability and performance.
Often, you will find that Interconnects are organized in hierarchies, with simply structures for on-chip communications (e.g. a bus), with more elaborate structures as the system scales. For example: Within a chip, a bus can be used, then four chips can be connected by a bus, and the four-chip assembly is connected to other 4-chip assembly via a switch.
Note that some modern chips have become so complicated, that even within a chip some elaborate interconnect is used.

## Slide 11: Option 1: Limiting Coherence Domain
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Memory
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Interconnect
Memory
Memory
Used to move data among systems
Coherence domain
Notes: Every cc-NUMA system should be configured with this option. Nowadays, many systems use partitioning as part of a cloud environment, so this option, even though it is not what the system is sold for, ends up more or less what happens in reality. Keep in mind that not all applications can scale up to a large cc-NUMA system. An interesting question is whether all the work on cache coherence and consistency is paying off when only a few select users (mostly traditional database systems) can use it.

## Slide 12: Option 1 Implementation
Each coherence domain has its own operating system
Systems can cooperate at the program level, with infrastructure implemented by the OS/Interconnect
  Message passing (e.g. MPI)
  Remote Direct Memory Access (RDMA)
Messages or RDMA accesses are implemented by the OS and use the Interconnect for fast data transfer
Advantages
  Simplicity
  No need for OS-level data placement headaches
Disadvantages
  Burden is shifted to the programmer
  Not all applications are designed to benefit (e.g. databases)

## Slide 13: Option 2: Use Broadcast to implement cc-NUMA
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Memory
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Interconnect
Memory
Memory
Broadcast used for cache coherence
much like a bus, using many 1-1 msgs
Notes: In this option, the cache coherence is maintained using broadcasts that propagate through the system using 1-to-many messages, in reality implemented on top of the interconnect. For example if the interconnect is a switch, a message is sent to the switch and from there it is replicated along all the downlinks to the recipients. Other implementations on different topologies for the interconnect are plausible. This approach was used (with some practical variations) on the IBM large POWER-based servers. The logic here is that the majority of users will not have applications that will scale to the extent of the large server. Thus, partitioning into sub-coherence domains will be the norm according to this model of thinking. Thus, simplification of the hardware is gained at the expense of limiting scalability and poor performance for applications that scale to the full extent of the server. However, the thinking was given that very few of these applications exist, it makes sense to focus on optimizing the software for those applications and reduce the cost and complexity of the hardware. Generally speaking, the approach did not fare very well, but it is difficult to tell whether this commercial lackluster performance is due to this issue or other, perhaps more important issues (like, the sparse software stack).

## Slide 14: Option 2 Implementation
The entire system is under one coherent domain.
Caches use the same simple protocol of bus-based systems, except it is now superimposed on a non-broadcast interconnect.
The protocol, however, needs to be modified because two caches may initiate a broadcast at the same time, and some arbitration and ordering will be needed to avoid race conditions.
Advantages
  Simplicity of hardware
Disadvantages
  Inherently non scalable
  Protocol has to be redesigned to avoid race conditions

## Slide 15: Option 3: Directory-Based cc-NUMA
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Memory
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Interconnect
Memory
Memory
Directory
Notes: This cartoon shows in an abstract way the implementation with the directory being a separate component that is attached to the Interconnect. This is done for illustration only, no real system implements directories this way. A directory-based solution reduces the messages between caches to implement cache coherence, but they create their own headaches.

## Slide 16: Directory Structure
Line 0
Line 1
Line M/L
A bitmap showing for a each
line which cache holds it
If line 0 is cached in cache 2
and 3, then bits 2 and 3 are
set to 1. Others, 0.
For memory of size M, and for
a line size L, we have M/L lines
The size of each entry includes
a modified bit and a bit for each
Independent L2 cache
Modified bit

## Slide 17: Recall: A Cache Miss on Read: Data Uncached
L2 Cache
L1
L1
L1
L1
Memory
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Read, addr
Read, addr
data
M=0, S=0, E=1, V=1

## Slide 18: Cache Miss on Read
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Memory
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Interconnect
Memory
Memory
Directory
Read, addr
Mem
Read, addr
M=0, S=0, E=1, V=1
Data
Notes: This cartoon shows in an abstract way the implementation with the directory being a separate component that is attached to the Interconnect. This is done for illustration only, no real system implements directories this way. A directory-based solution reduces the messages between caches to implement cache coherence, but they create their own headaches.

## Slide 19: Recall: A Cache Miss on Read: Data Cached
L2 Cache
L1
L1
L1
L1
Memory
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Read, addr
M=0, S=1, E=0, V=1
M=0, S=0, E=1, V=1
data
M=0, S=1, E=0, V=1

## Slide 20: Option 3: Directory-Based cc-NUMA
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Memory
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Interconnect
Memory
Memory
Directory
Notes: This cartoon shows in an abstract way the implementation with the directory being a separate component that is attached to the Interconnect. This is done for illustration only, no real system implements directories this way. A directory-based solution reduces the messages between caches to implement cache coherence, but they create their own headaches.

## Slide 21: Recall: A Cache Miss on Read: Data Dirty
L2 Cache
L1
L1
L1
L1
Memory
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Read, addr
M=0, S=1, E=0, V=1
M=1, S=0, E=1, V=1
M=0, S=1, E=0, V=1
data

## Slide 22: Virtualization Structure
Source: NSI

## Slide 23: Birth of Cloud Computing
“Amazon had a lot of machines that stay idle except during holidays”:
Started to provide the ability to “rent” capacity
The concept of an “image” and SaaS
Clients pay per usage (rent vs. own model)
Add capacity on the fly to respond to change in workload (“Elastic” cloud)
Later on, became an industry standard
Software also adopted the rent vs. own model
Clients did not need to run their own systems
Successful example: Netflix
Power savings

## Slide 24: The Case For Virtualization
Advantages:
Ability to run different operating systems
Ability to run different versions of the same operating system
Preservation of software investments
Faster startup
Better resilience
Faster development cycle for system software
Better sharing of I/O equipment
Lower hardware costs
Lower management cost

## Slide 25: The Case Against Virtualization
Disadvantages:
Added overhead
Slowdown especially in I/O performance
Added complexity

## Slide 26: How Does it Work?
Hypervisor manages the hardware
Runs operating systems as user level processes
User programs (applications) run also as user level processes controlled by their corresponding operating systems
User program interactions:
  Interrupts
  Exceptions
  System calls
Operating system interactions
  Interrupts
  Privileged instructions
  Direct access to hardware registers and resources
  Memory management
  I/O device access and drivers

## Slide 27: Memory Management
Each OS expects memory to start at frame 0.
This can be done in 2 ways (among others)
  Method 1: Have an additional level of translation of page table addresses at the control of hypervisor. Each OS is given control over a range of frames. Translation ensures that OS sees frames starting at 0
  Method 2: Via trapping OS manipulation of page table and adjusting dynamically by the hypervisor