## Slide 1: System Architecture and Performance
CS 258
Week 1: Introduction to performance

## Slide 2: Introductions
Professor, CMU, USA 93—97
Senior Manager, IBM Research, USA, 97—12
Adjunct Professor, UT Austin, USA, 98—12
Dean, KAUST, 12-20
Special advisor to president, KAUST, 20-21
Professor, KAUST, 21-
Visiting scholar:
  Bell Labs 94-97, Bellcore, 94-97, Meta (Facebook) 22
Research:
  Systems, distributed systems, resilient computing, security, system architecture, performance, parallel processing
Fellow of IEEE, Fellow of the US National Academy of Inventors, Fellow of the AAIA
Instructor: Mootaz Elnozahy
BSEE ‘84, MCE ‘87, MSCS ‘90, Ph.D ‘94
CS 258: Sys Arch & Perf
Office hours: by appointment, 4111, Bldg 1
Class time: Mon-Thu: 16:00—17:30, Rm 3123, Bldg 9

## Slide 3: Introductions
Your name
Your degree, program, advisor (if any)
Background (country, university, undergraduate degree)
Did you take courses in:
  Computer architecture?
  Operating systems?
Why are you taking this course?
What would you like to achieve by the end of this course?
Notes: Please tell me your background so that I can adjust throughout the semester.

## Slide 4: Goals
To start thinking systems instead of components
To understand how systems are structured and how they work
To acquire skills in performance evaluation techniques
To acquire some practical skills with performance evaluation tools
Notes: The most important outcome of this class should be a new way of thinking. It is not about the parts or even the sum of the parts. It is about trying to master complexity, which is a skill that will be needed regardless of whether you will continue in academia for more advanced degrees, or if you take a job in industry (or academia after you graduate). The class is fairly divided into two big halves: Architecture and performance evaluation. There will be some emphasis on hands-on skills.

## Slide 5: Relevance
In real life, resources are finite. Efficiency is not optional.
Writing better code
Better system architecture
Performance debugging
Decision support
Notes: Most of us will not design systems. Most of us have to work with pre-existing designs. For a good majority of us, we will be just writing code. However, understanding how the system works will make you write better code. If you understand the limits on cache performance and memory bandwidth, it is hoped that you will be able to pick the right algorithm for both the problem and the system. Similarly, understanding how runtime systems work, you will hopefully make the write choice of which programming language should be used for which particular situation, and so on.

## Slide 6: Lecture Style and Your Role
The class is interactive. You need to participate.
Participation is not graded, but is essential to get something out of the lecture
Don’t be shy
Show respect to your colleagues
There are no stupid answers
Silence is not a virtue
Notes: Class interaction will keep you in the flow of the material. This is not about you receiving information from me: Rather, this is more about you applying your critical thinking to come up with the information on your own. This is my philosophy in teaching and it has worked well since 1993.

## Slide 7: Administrative
Office hours by appointment. You are encouraged to book office hours, especially if you are struggling
Grading:
  Homework: 30% (teamwork, individual)
  Project: 25% (teamwork)
  Exam (3): 45% (individual)
Copying resources, solutions, etc.
  OK, provided that: 1) Attribution is made, 2) you understand what is being copied
Cheating:
  You will fail the course with an F
Notes: I would like to emphasize here the importance of shouldering your responsibility. You are all graduate students now. So, people who are not pulling their weights in homework or project will be penalized.

## Slide 8: What is a System?

## Slide 9: Definition (?)
System level thinking looks at the solution in its totality, avoiding pigeonholing onto one layer or component
System architecture is all about the interactions of the various layers and how they impact one another
Goal: To start thinking at the system level to achieve the best outcome
Algorithm
Code
Runtime/Libraries
Operating system
Hardware
Processors
Memory
Interconnects
I/O Devices
Notes: Often, the best solution is obtained at the algorithm level. I observed in my careers sometimes a factor of 4 improvement by simply picking a better algorithm. A factor of 4 improvement out of the same components is a huge improvement. It is important also to appreciate how difficult the problem is in terms of handling complexity: Sometimes 5% improvement is all that is between a product success or failure. There are many aspects of course, but it helps to understand that your approach has to be comprehensive to the extent that is possible.

## Slide 10: Examples from Real Life

## Slide 11: 64,000 CPU Registers?
You are leading a big project to design the next supercomputer
You have a budget of $20M/year for an exploratory design
Bob approaches you with a clever circuit design idea yielding 64K registers
Typical processors have a few architecture-level registers, and a few hundred microarchitecture registers
This is 3 orders of magnitude improvement!!!
Bob is asking for 3FTE’s to work with him on the idea ($600K). Do you fund Bob?
Real Story!!
Notes: Several flaws are to be seen here: 1) The proposal is based on intuition (more registers  better performance). 2) Lack of any metric of improvement at the application level. 3) No quantitative analysis to show the existing problem that is being solved (I am not talking about a quantitative analysis of the solution, but rather, the problem). It is important before stating a solution to understand what is the problem that is being solved!!

## Slide 12: 64K Registers
Algorithm
Code
Runtime/Libraries
Operating system
Hardware
Processors
Memory
Interconnects
I/O Devices
Let us discuss the tradeoffs
Notes: In this discussion, we have shown that most programs will not be able to benefit from increasing the number of registers beyond a certain limit. Experience has shown that between 32 to 64 is about the sweet spot for what a program needs for most cases. The way the proposal was stated did not open the discussion for potential other uses for the added registers: For instance, enabling more hardware threads could be a plausible use for this technology.

## Slide 13: Bigger Picture: Performance & Other Things
CPU
CPU
CPU
Interconnect
MEM
MEM
MEM
PCI
PCI Bus
GPU
GPU
MEM
MEM
CPU
CPU
CPU
Interconnect
MEM
MEM
MEM
PCI
PCI Bus
GPU across the PCI bus
GPU integrated in CPU
Which is better?
Notes: We examine here two different methods for building systems that contain GPU’s in them. In the first, the GPU’s are mounted as independent chips on the I/O bus. In the second, the GPU’s are integrated into the CPU, often with an instruction set extensions. There are many tradeoffs that exist here, and it is important to notice the title “Other Things”. Performance alone is not the deciding factor in the success of a particular design or the lack thereof. The first style is what NVIDIA uses, whereas Intel and IBM tried the second design several times and failed. Of the reasons: Having different chips allows the design more freedom to add processing units and to be architecture-independent, which is important for software portability (a huge factor that is often more important than performance—people are more expensive than hardware). It also meshes nicely with the need of having at least one graphic processor to control the display of the machine. The first configuration incurs a substantial performance and power overhead because the data have to be copied from the CPU’s main processor to the GPU and back. Therefore, this works well when you have a bulk of data to be processed, such as in graphics or in AI. But it will not perform well when there are small morsels to be processed.

## Slide 14: Streaming (no, not Netflix!)
for(i = 0; i < n; i++)
c[i] = a[i] x b[i]; (this is called the STREAM benchmark, after John D. McCalpin)
Information:
a, b, and c are vectors of type “double”
n is very large
Let us look at a system level approach to this problem
Notes: The stream benchmark is a standard benchmark for assessing memory bandwidth. It is often quoted when performance of real applications is concerned. The benchmark presents an extreme case of relying on the memory bandwidth for performance. It features no reuse of data, and loads 24 bytes for every operation. This renders the cache hierarchy on the processor all but useless, and pushes the requirements on the memory bandwidth to its arguable maximum.

## Slide 15: The problem
for(i = 0; i < n; i++)
c[i] = a[i] x b[i];
Algorithm
Code
Runtime/Libraries
Operating system
Hardware
Processors
Memory
Interconnects
I/O Devices
Notes: This particular benchmark represents a very simple algorithm and code. It does not require much in terms of operating system or library support. The code is very simply that the compiler cannot do much about it. Therefore, the benchmark’s raw performance centers around the hardware, and more specifically the memory and interconnect bandwidth.

## Slide 16
 | Z-100 | Z-200 | ZV-100
Speed | 3GHz | 3GHz | 3GHz
No of FPU’s | 2 | 2 | 4
Instruction issue | 2 | 2 | 2
L/S units (8-bytes) | 2 | 2 | 4
Prefetcher | 16 ahead | 16 ahead | 32 ahead
L1 cache (2 cycles) | 32K | 32K | 32K
L2 cache (5 cycles) | 1MB | 4MB | 8MB
Memory bus | 3GB/sec | 3GB/sec | 6GB/sec
Vector instructions | No | No | 4-way
Cost | $1500 | $2200 | $10,000
Which one do you pick?
L1: ld r1, (r4) # a[i]
ld r2, (r5) # b[i]
fmul r3, r1, r2 # a x b
st r3, (r6) # c[i]
add r4, 8
add r5, 8
add r6, 8
add r0, -1 # i
bne L1
L1: ld v1, (r4)
ld v2, (r5)
fmul v3, v1, v2
st v3, (r6)
add r4, 32
add r5, 32
add r6, 32
add r0, -4
bne L1
Notes: In this solution, we wanted to go into analyzing the program at a lower level. Experienced engineers typically have more straightforward ways of assessing the problems, potentially using high level tools. This example is simply serving a particular need which is to ensure a thorough understand of what happens when a program executes in the processor and the implied pressure that it will exert on the various resources (cache, memory bandwidth, etc.). (Note, the Z-100, Z-200 and ZV-100 are not real processors)

## Slide 17
 | Z-100 | Z-200 | ZV-100
Speed | 3GHz | 3GHz | 3GHz
No of FPU’s | 2 | 2 | 4
Instruction issue | 2 | 2 | 2
L/S units (8-bytes) | 2 | 2 | 4
Prefetcher | 16 ahead | 16 ahead | 32 ahead
L1 cache (2 cycles) | 32K | 32K | 32K
L2 cache (5 cycles) | 1MB | 4MB | 8MB
Memory bus | 3GB/sec | 3GB/sec | 6GB/sec
Vector instructions | No | No | 4-way
Cost | $1500 | $2200 | $10,000
Which one do you pick?
Importance of quantitative thinking: Metrics
- Maximum performance
- Performance/$
Notes: Metrics are important: Even the word “Maximum performance” is vague. Performance can mean 1) The time it takes for a program to finish (also known as response time, latency, etc.). It is measured in time (seconds or sub-seconds). 2) The amount of processing that a system performs (usually measured by instructions/per seconds, or operation/seconds. Often called throughput and is measured by ops/seconds).

## Slide 18
 | Z-100 | Z-200 | ZV-100
Speed | 3GHz | 3GHz | 3GHz
No of FPU’s | 2 | 2 | 4
Instruction issue | 2 | 2 | 2
L/S units (8-bytes) | 2 | 2 | 4
Prefetcher | 16 ahead | 16 ahead | 32 ahead
L1 cache | 32K (1 cycles) | 32K (1 cycles) | 32K (1 cycles)
L2 cache | 1MB (5 cycles) | 4MB (10 cycles) | 8MB (10 cycles)
Memory bus | 3GB/sec (60 cycles) | 3GB/sec (60 cycles) | 6GB/sec (60 cycles)
Vector instructions | No | No | 4-way
Cost | $1500 | $2200 | $10,000
L1: ld r1, (r4) # a[i] CYCLE 1
ld r2, (r5) # b[i] CYCLE 1
fmul r3, r1, r2 # a x b CYCLE 2
st r3, (r6) # c[i] CYCLE 3
add r4, 8 CYCLE 3
add r5, 8 CYCLE 4
add r6, 8 CYCLE 4
add r0, -1 # I CYCLE 5
bne L1 CYCLE 6
Notes: Several assumptions are made here about the sophistication of the instruction-issue unit. In particular, this is a simple in-order processor (instructions are not reordered for better execution like what you will see in modern processors). Also, we make an assumption that the compiler does not do any loop runrolling or fusion. Again, this is done for illustrative point only and not as a representative of a real system.

## Slide 19
 | Z-100 | Z-200 | ZV-100
Speed | 3GHz | 3GHz | 3GHz
No of FPU’s | 2 | 2 | 4
Instruction issue | 2 | 2 | 2
L/S units (8-bytes) | 2 | 2 | 4
Prefetcher | 16 ahead | 16 ahead | 32 ahead
L1 cache | 32K (1 cycles) | 32K (1 cycles) | 32K (1 cycles)
L2 cache | 1MB (5 cycles) | 4MB (10 cycles) | 8MB (10 cycles)
Memory bus | 3GB/sec (60 cycles) | 3GB/sec (60 cycles) | 6GB/sec (60 cycles)
Vector instructions | No | No | 4-way
Cost | $1500 | $2200 | $10,000
Analysis: Z200
How much reuse do we have?
for(i = 0; i < n; i++)
c[i] = a[i] x b[i];
L1: ld r1, (r4) # a[i] CYCLE 1
ld r2, (r5) # b[i] CYCLE 1
fmul r3, r1, r2 # a x b CYCLE 2
st r3, (r6) # c[i] CYCLE 3
add r4, 8 CYCLE 3
add r5, 8 CYCLE 4
add r6, 8 CYCLE 4
add r0, -1 # I CYCLE 5
bne L1 CYCLE 6
Notes: Here, we start by eliminating the obvious case where two identical processors except in cache size are compared, with the workload not needing any caching, we decide to withdraw Z-200 from the comparison.

## Slide 20
 | Z-100 | ZV-100
Speed | 3GHz | 3GHz
No of FPU’s | 2 | 4
Instruction issue | 2 | 2
L/S units (8-bytes) | 2 | 4
Prefetcher | 16 ahead | 32 ahead
L1 cache | 32K (1 cycles) | 32K (1 cycles)
L2 cache | 1MB (5 cycles) | 8MB (10 cycles)
Memory bus | 3GB/sec (60 cycles) | 6GB/sec (60 cycles)
Vector instructions | No | 4-way
Cost | $1500 | $10,000
Analysis: Z-200
The large cache of Z-200 buys me nothing for the code below
for(i = 0; i < n; i++)
c[i] = a[i] x b[i];
L1: ld r1, (r4) # a[i] CYCLE 1
ld r2, (r5) # b[i] CYCLE 1
fmul r3, r1, r2 # a x b CYCLE 2
st r3, (r6) # c[i] CYCLE 3
add r4, 8 CYCLE 3
add r5, 8 CYCLE 4
add r6, 8 CYCLE 4
add r0, -1 # I CYCLE 5
bne L1 CYCLE 6

## Slide 21
 | Z-100 | ZV-100
Speed | 3GHz | 3GHz
No of FPU’s | 2 | 4
Instruction issue | 2 | 2
L/S units (8-bytes) | 2 | 4
Prefetcher | 16 ahead | 32 ahead
L1 cache | 32K (1 cycles) | 32K (1 cycles)
L2 cache | 1MB (5 cycles) | 8MB (10 cycles)
Memory bus | 3GB/sec (60 cycles) | 6GB/sec (60 cycles)
Vector instructions | No | 4-way
Cost | $1500 | $10,000
Analysis: Z-100
From the instruction stream, at best 1 FP operation
per 6 cycles
Each 1 FP operation produces 24 bytes of activity on the
memory bus
We need 24 bytes/6 cycles, or 4 bytes/cycle
But the bus can supply only 1 byte/cycle!
Assumptions: Perfect prefetching, caching, etc.
L1: ld r1, (r4) # a[i] CYCLE 1
ld r2, (r5) # b[i] CYCLE 1
fmul r3, r1, r2 # a x b CYCLE 2
st r3, (r6) # c[i] CYCLE 3
add r4, 8 CYCLE 3
add r5, 8 CYCLE 4
add r6, 8 CYCLE 4
add r0, -1 # I CYCLE 5
bne L1 CYCLE 6
Notes: The 24 bytes of activity on the memory bus come from the need to load a[i] and b[i], both of type ”double” which is 8 bytes, totally 16 bytes of loads. Also, we need to write c[i], which adds 8 bytes of data from the processor into memory, rounding up the 24 bytes.

## Slide 22
 | Z-100 | ZV-100
Speed | 3GHz | 3GHz
No of FPU’s | 2 | 4
Instruction issue | 2 | 2
L/S units (8-bytes) | 2 | 4
Prefetcher | 16 ahead | 32 ahead
L1 cache | 32K (1 cycles) | 32K (1 cycles)
L2 cache | 1MB (5 cycles) | 8MB (10 cycles)
Memory bus | 3GB/sec (60 cycles) | 6GB/sec (60 cycles)
Vector instructions | No | 4-way
Cost | $1500 | $10,000
Analysis: ZV-100
From the instruction stream, at best 4 FP operation
per 6 cycles
Each 1 FP operation produces 24 bytes of activity on the
memory bus
We need 96 bytes/6 cycles, or 16 bytes/cycle
But the bus can supply only 2 byte/cycle!
Assumptions: Perfect prefetching, caching, etc.
L1: ld v1, (r4)
ld v2, (r5)
fmul v3, v1, v2
st v3, (r6)
add r4, 32
add r5, 32
add r6, 32
add r0, -4
bne L1

## Slide 23: Conclusion
For the problem at hand, the memory bus (bandwidth) is the bottleneck
A more sophisticated compiler, a longer pre-fetch or a larger cache would be ineffective
The computation speed is defined by the memory bus bandwidth:
  Z100 will deliver about ½ the performance of ZV-100
  Z100 is the choice if the metric is performance/$
  ZV100 is the choice if the metric is purely performance
Questions to ponder: Are the caches useful? Is the system balanced?

## Slide 24: Don’t let Complexity Defeat You!
for(i = 0; i < n; i++)
c[i] = a[i] x b[i];
Information:
a, b, and c are vectors of type “double”
n is very large
With experience, you would be able to quickly determine the bottleneck. In this case, you can see that 24/bytes/op are needed. Many architects use metrics like these to identify the “capacity” of a processor, or as design parameters

## Slide 25: Observations
The Z-100 processor was capable of 6GF/sec peak performance
  How much of that was possible in the previous example
The Z-300 will be available in three months, with 12GB/sec memory bus instead of 3GB/sec. Will the performance quadruple?
What if memory bandwidth is no longer the bottleneck, what is the next bottleneck?

## Slide 26: Another Example from Real Life
a[i, j] @ (t+1) = f (a[i+1, j], a[i-1, j], a[i,j], a[i+1, j-1], a[i+1, j], a[i+1, j+1], a[i-1, j-1], a[i-1, j], a[i-1, j+1]) @ t

## Slide 27: Example Code
for(i = 1; i < m - 1; i++)
for(j = 1; j < n - 1; j++)
b[i,j] = a[i,j] + a[i+1, j] + a[i-1, j] + a[i, j+1] + a[i, j-1];
What are the similarities and differences from the previous problem?
- Each line will put pressure on the memory bandwidth
- There is considerable reuse (caching comes to play)

## Slide 28: Definition (?)
Algorithm
Code
Runtime/Libraries
Operating system
Hardware
Processors
Memory
Interconnects
I/O Devices
Here, it is not just the memory bandwidth that need to be looked at, but also the cache.
Caching and memory bandwidth interact closely
In this case, the approach has to be more comprehensive
An elegant solution was found at the algorithm level: Cache-oblivious algorithm and cache-aware algorithm

## Slide 29: Recap
Many performance problems come from focusing on one aspect of the system without understanding the interactions among system components
Look for the bottlenecks first, and be ready to try to estimate the aspect of one solution over the entire system
It is not always the best technology that wins (e.g., Intel, NVIDIA). Companies that understand the hardware and software together often make sound decisions commercially even if suboptimal technologically