## Slide 1: System Architecture and Performance
CS 258
Week 07: Cache consistency and coherence

## Slide 2: The Quest for Performance Continues
Vertical scaling (Single thread performance)
  Instruction-level parallelism
    Limitations were studied with pipelining
  Frequency
    Power limitations
Horizontal scaling (multithreading, multicore, multiprocessor)
  The only way to get performance is to spread the work over more processing elements
Processor Chip
Core 0
Core 1
Core 2
Core 3
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Memory
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Interconnect
Memory
Memory
Notes: In the 1980’s, instruction-level parallelism was presented as the panacea that will enable programmers to write sequential code and let the compiler extract performance through instruction-level parallelism. The people in the 1980’s were not stupid. The parameters of a typical system encouraged this line of thinking: The memory access was more or less what it is today in terms of latency, and the processor cycle back then was measured in sub microseconds, not nanoseconds. So, cache misses did not constitute the big problem that it is today. Similarly, a TLB back then was designed with timing characteristics that were very different than today. All being said, it became quickly clear by the beginning of the 1990’s that the memory subsystem came to dominate the performance of most practical applications. The memory latency did not improve much over the years, while processors continued to get faster until around 2002—2003, when the quest stopped. The current balance of a typical system puts more emphasis on TLB and cache performance. GPU’s are a notable exception, but this comes from a class of applications where the emphasis is on integer/floating point performance. Yet, programming these systems is not particularly easy, and they are horrendously inefficient when it comes to power consumption.
When the frequency improvement stopped, the improvement in silicon translated to more areas of circuits that are switched at around 1—3GHz. Engineers translated this first into larger caches, but there is a certain size beyond which the return on the investment diminishes. In a fitting tradition, the industry started moving toward adding more cores on the processor chip, ushering the era of multicore processors. The onus is transferred to the programmer, who has to write code that explicitly expresses the parallelism in the application (if any). This proved to be a daunting task. Writing parallel applications, much less debugging them, proved to be very difficult. Today, most of the benefits from having multicore processors comes from partitioning the chip into different processing domains in a cloud computing environment.

## Slide 3: Weak Scaling vs. Strong Scaling
In horizontal scaling (adding more processors) I can either
  Solve a larger problem at a certain time, or
  Solve the same problem faster
Weak scaling:
  Useful in physics, databases, etc. For example, climate prediction code uses horizontal scaling to add more accuracy in weather prediction
Strong scaling:
  When we have performance-critical applications
Notes: A relevant example here is the weather prediction or modeling, or atmospheric modeling in general. The problem divides the atmosphere into cubes of a certain size, and then use finite element analysis and traditional partial differential equation solvers to model the weather. The accuracy of the results depend on the size of the cube (sometimes called cell). In this case, a new generation with more processors enable the cell size to go smaller (5 km was the norm a few years ago, and this keeps improving). This is an example of weak scaling: We are not running the problem faster, but we are obtaining other benefit (e.g. more accurate modeling).
Strong scaling is about solving the same problem but faster. Today, this is a very challenging undertaking. In general, strong scaling puts all the pressure on the interconnect and the programmer. Adding more processors will not help unless the interconnect scales accordingly (or even at a faster rate, because there are some non-linear queueing effects that govern interprocess communications).

## Slide 4: Example: Multithreading
int shared;
main() {
t0 = CreateThread(fn);
t1 = CreateThread(fn);
JoinThread(t0);
JoinThread(t1);
cout << shared << endl;
}
Void fn() {
shared++;
} }
Notes: This is a fun exercise to show you how it can be problematic to write seemingly innocent code. In this case, the variable ”shared” is shared between two threads, but incrementing the variable is not an atomic operation on current systems. In the above example, the variable ”shared” at the end of the computation can be 1, or 2. The introduction of “JoinThread” ensures that the main thread does not race to finish before the two created threads have a chance to run.

## Slide 5: Consistency and Coherence
When data is shared and there are different copies then:
  Consistency: All copies are the same
  Coherence: Any read returns the most recent update anywhere
This model describes ”Sequential Consistency”
  The accesses to the data are equivalent to a single thread making modifications
Notes: Sequential consistency is defined as this: The concurrent execution of threads to produce results that are equivalent to running these threads sequentially, one after the other. Of course, if the threads were to run sequentially, we won’t need any synchronization or worry about data races. This would be the simplest programming model, but the performance will be terrible. The trick is to run the threads in parallel, exploiting multicores and multiprocessors, while ensuring that the outcome is exactly equivalent to some sequential interleaving of threads. Luckily, this is possible by exploiting the hardware, especially the caches. Most systems today employ a cache coherence protocol that ensures some form of consistency (Intel provides sequential consistency, IBM provides a faster model called processor consistency. The process consistency model, while faster than sequential consistency, it proved to be difficult for the programmers to master. Therefore, programmers became very conservative and inserted synchronization primitives throughout the code, effectively thwarting the benefit of the faster consistency mechanism. It is important to understand that the quest for performance will not win if the price is more programming complexity, at least in general. But there are nice linear algebra algorithms that show what researchers call embarrassing parallelism (meaning, high degree of parallelism). This motivated a company like NVIDIA to simply run the caches on the GPUs without coherence or consistency protocols.

## Slide 6: The Misguided Quest for Performance
Relaxed consistency models
  Processor consistency: Everything is consistent within the same processor
  Causal consistency: Consistency follows data dependence
  Entry consistency: Consistency guaranteed only at the entry of a critical section
  Weak consistency: Consistency is weakened according some rules (rr, rw, etc.)
  Insert your model here: Punt the problem to the programmer
The programmer said “thanks, but no thanks”
Notes: Running parallel programs is difficult. Debugging them is almost impossible. Restricted programming models such as transaction processing systems, or message-passing algorithms that do not share memory, can prove to be useful in such situation, but they do not perform as well as shared memory programming. Why? Because transaction processing does the scheduling of operations to provide parallelism without saddling the programmer with the management of parallelism. But as you can imagine, this means that the scheduling (which is NP complete) will not always exploit the parallelism like an experienced programmer does. Similarly, message-passing requires the programmer to think hard about the interactions, in addition to the performance overhead of packing and unpacking messages. Shared memory programming is simpler, but synchronization bugs are extremely difficult to uncover and they are generally not repeatable (they are sometimes called Heisenbugs, after the concept of the uncertainty principle of Heisenberg in quantum physics).

## Slide 7: Consistency & Coherence at the Cache Level
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Two-socket system with
2 4-core processors
A memory bus connects
all processors
We need to ensure that
if data is shared among
caches, that they are
consistent and coherent
Notes: The picture in the slide tells the story. It shows the simplest multiprocessor today (they are called a 2-socket system, where a socket is the substrate on which a processor chip is mounted). The caches at the L2 level play the role of synchronization managers.

## Slide 8: Snoop-Based Protocols: Update
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Caches are write-through
All updates go on the bus
All copies are kept the
same
This is an update based
protocol
What are the issues?
Notes: Snoop-based protocols are used when the number of chips is small. A bus connecting the chips becomes a practical and cheap solution. You will find snooping protocols to be used in low-end systems. Snooping also is likely to be used within the chip as well between the cores. In the picture, a shared cache is shown. But an alternative is to have a private L2 cache for every core, in which case they will run the synchronization protocol with the all the caches on the system, whether they are on the same chip or on the other chips.

## Slide 9: Cache Structure
The cache line is (generally) the unit of transfer from cache to main memory, or between cache levels
64-byte, 128-byte, 256-byte, … 1024-byte
address
address
address
address
address
address
M
E
V
Notes: The directory of the cache contains for every cache line the address that is being cached at that line. There are also 3 to 4 status bits: M is for modified, E is for exclusive, V is for valid. M = 0 when we bring the line into the cache from memory. It is set to 1 by the hardware automatically if the cache line is updated (any byte). E is 1 if the cache line is not cached elsewhere in the system. When E=1, the processor can generally write to the cache line. However, if E=0, the write cannot proceed, because the other copies that are cached in other caches have to be invalidated or written to in parallel. V = 1 if the cache line is valid. It is set to 1 when the cache line is brought from amin memory and set to zero when the line is invalidated. Often, a fourth bit called S is added to the mix. S=0 if the line is not cached elsewhere. IT is set to 1 if there are other copies in other caches in the system. If S=1, then no writes can proceed. S=1 signifies a read-only mode of sharing.
The cache line size is an important design decision. A larger cache line works best if the code is showing a high degree of locality, as it reduces the overhead of bringing the data from memory (the overhead is amortized over a larger amount of data). It also means a smaller number of lines in the cache, and accordingly a smaller directory structure. On the other hand, a larger cache line can introduce complexity because the bus may not be able to move the data in a single cycle, in which case we say that the cache line is sectored. The sectors are effectively a way of partitioning an otherwise large cache line. A large cache line can also create a problem in the case of false sharing (see later).
The cache directory typically contains the physical address of the line that is being cached. Because the directory is designed out of expensive (area and power) static circuits, we would like to reduce the amount of storage that is necessary. This is why we do not store the offset of the cache line. In other words, if the physical address space is 44 bits, and the line size is 64 bytes, then there is no point in storing the lowest 6 bits (which define which byte within the line) in the directory structure. So the entries will be only 38 bits in width (and yes, we try to save as many bits as possible, there is no rounding to bytes).
The directory can be organized as direct mapped or set associative. It all depends on the hashing function that is used to find the elements in the cache. In a direct mapped cache there is only one entry corresponding to a certain hash value. In a set associative cache, a hash function points to the entire set. Within the set, it is fully associative, meaning that we do an all comparisons on the same tags within the set.
The cache directory is an example of what some call CAM: Content Addressable Memory, because we access the memory based on its content. Minor detail.

## Slide 10: Snoop-Based Protocol: Invalidate
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
To write: Send an invalidate
request on the bus:
- The cache line is owned by
someone else, the someone
else will send the recent copy
and invalidates its own
To read: Send a read
request on the bus:
- The cache line is owned by
someone else, the someone
else will send the recent copy
and marks its own copy as
shared
Often called: The MESI protocol (Modified, Exclusive, Shared, and Invalid)
Notes: At the beginning of the multiprocessor era, there was a debate about whether it was better to invalidate copies in other caches or simply update them. Because these systems were small and slow, the difference was not pronounced. However, as the systems started growing in size and speed, it became clear that trying to continuously update all the shared copies will not scale up and the performance will suffer. Today, almost all processors use invalidation when they want to write into a shared cache. The writer asks all the other holders of the same cache line to invalidate their copies so that it can proceed to write on its own without interference.

## Slide 11: On The Road to Hell: False Sharing
int shared[2];
main() {
t0 = CreateThread(fn, 0);
t1 = CreateThread(fn, 1);
JoinThread(t0);
JoinThread(t1);
cout << shared << endl;
}
Void fn(int i) {
shared[i]++; // More code to access and update shared[i] follows
} }
Notes: It is easy to get tripped in performance if the programmer does not understand how caches work. A cache line can hold data that are accessed by two different threads, even though that the threads are actually not sharing anything. In this case, the invalidate protocol will result in a ping pong effect where on every write by a thread, spurious invalidation requests are made to all the other caches that are holding the same line. False sharing must be avoided at all costs.

## Slide 12: On the Road to Hell: What about L1?
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Notes: If the L2 caches manage the coherence protocols, how do we ensure that the caches at the L1 level are going to remain coherent? The complexity now increases, as the controller of the L2 cache will also invalidate copies in the L1 in the case of invalidation, and the L1 has to mimic the same state as the corresponding L2. It pays here to have an inclusive L2 cache.

## Slide 13: On the Road to Hell: What about L3?
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
L3 Cache
L3 Cache
Notes: And if there is an L3, the L2 will also have to propagate the invalidate requests and other cache requests on the system. An inclusive L3 cache is simpler here to deal with than a victim cache. Typically, victim caches have to participate directly in the coherence protocol, causing a lot of complexity.

## Slide 14: Limitations on Snooping: What if no Bus?
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Memory
Memory
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
L1
Interconnect
Memory
Memory
Notes: There are two problems with buses: They do not scale as the bandwidth is divided among multiple processors. Also, physically, a bus cannot extend beyond a certain length, as the signal attenuation can become a problem if the bus length exceeds a certain limit (essentially, it becomes a transmission line with the headaches that come with that, EE students may appreciate this )
Cc-NUM systems, as shown in the figure, introduce their own set of problems. It is important for the operating system to schedule the threads near that data that will be accessed by these threads. A chip accessing its local memory will experience better latency than if it were to fetch the data from a remote memory bank as this will require that the data travel through the interconnect, versus the attached memory bus for local memory. Large servers today are effectively all NUMA.