## Slide 1: System Architecture and Performance
CS 258
Week 3: Introduction to the modern CPU

## Slide 2: Historical Perspective & Trail of Tears
Moore’s Law, 1965—Now (but how much longer)
  The law is about lithography (shrinks by x2 every 18 months)
  Today, we are in 5nm (soon 3nm).
  Molecule sizes is 0.2nm, so we may have four more generations, at best
Yield is proportion of of chips on the wafer that are good
Each processor chip is tested on the wafer and then when alone
Size 10-20mm x 10-20mm
Cost of the chip is: Cost of design + cost of manufacturing + cost of testing + cost of packaging
It used to be: Smaller transistor  faster switching, but no more since 2003.
Notes: As we move to smaller and smaller transistors, the yield out of the chip drops, the cost of the chip will go up, and at some point (like when the frequency stopped growing in 2003), we will not be able to shrink the device further. What will happen next will be interesting to see: 1. Silicon survives but the growth moves from planar devices to three-dimensional devices and potentially three-dimensional chips, or 2) A whole new technology is introduced (e.g., carbon tubes). Experience has shown time and again that betting against silicon since the 1950’s has been a losing proposition. Will Silicon dominate the next year of processing? You will hopefully see this play out during your careers 
Why is the wafer circular while the die is square? Isn’t it wasteful of wafer area? Yes it is! However, the process by which a wafer is fabricated depends on a centrifugal depositing of silicon and produces a cylinder-like structure that is cut horizontally into wafers.

## Slide 3
Loader
Execution Units
(Pipelined)
State
Instruction Cache
Instruction Decode & Op Issue
Load/Store Unit
Memory (Caches, memory controller, bus interface)
Main ideas: Multithreading, pipelining, branch prediction, out of order execution, prefetching,
I/O
Notes: These are the building blocks of a modern processor. Nowadays, processor chips are said to be multi-core, which means that there are multiple CPU’s on the chip. Each core has the conceptual picture of the above figure. Chip designers since 2003 have been translating the technology advances in lithography into more cores per chip. This adds more processing power, but strains the memory bandwidth. Additionally, a programmer today is faced with stagnant single thread performance, and the only way to get more performance is to write parallel programs.

## Slide 4: Multithreading
What?
  Abstractions of independent instruction streams implemented in hardware, equivalent to a CPU from a software perspective
Why?
  Ideal for tolerating memory latency in the case of cache misses
  Can be exploited by software: E.g., Assist Threads
How much?
  Additional processor state: Registers, TLB, etc. (cost & power)
  Competition for resources on the pipeline, cache, memory bandwidth, etc.
Notes: A hardware thread is essentially the abstraction of a CPU. The hierarchy is like this: Chip  {cores}, and then Core  {threads}. The threads in a core each has registers, TLB, etc., but share the pipeline, the cache, the memory bandwidth of a single core. More threads will tolerate memory latency during cache and TLB misses, but there is no free lunch. Competition among threads can impact single thread performance. If the code is well behaved, it may be a good idea to turn off multithreading on the core on which it runs. But this is difficult to do in practice (what is well behaved is a very interesting question).

## Slide 5: More on Multithreading
Implications for the operating system: Scheduling
Implications for performance: More throughput, but not faster!
Implications for the software writer: May want to exploit by assist threads, etc.
A confusing concept: Program level threads can be multiplexed on the hardware threads
Notes: With hardware multithreading, the operating system effectively has more processors to schedule, where each hardware thread is treated by the operating system as a processor of its own.
While hardware multithreading was initially introduced to tolerate the latency of cache memory, it is a means for increasing the throughput of the processors, meaning, more instructions per seconds are executed. However, the individual threads themselves do not run any faster than a single thread.
To get performance out of multithreading, it is up to the programmer to use the threads to improve performance. However, hardware multithreading is not really great for performance when used in this manner. Recall that the threads on each core compete for pipeline cycles, cache memory, memory bandwidth, and TLB resources. So if all hardware threads are active simultaneously, it would be the case that they are going to run slower. If you really want performance out of multithreading, the threads have to be distributed across different cores.

## Slide 6: A Software Picture
User Program
User Program
User Program
User Program
Processor Chip
Core 0
Core 1
Core 2
Core 3
Hardware
threads
Operating System 0
Kernel
threads
Operating System 1
Kernel
threads
User Program
User
threads
Hypervisor
Hypervisor
threads
Notes: Threads exist as abstractions at different levels. At the user level, these are programming constructs that give the illusion of running in parallel. At the operating system levels, the illusion at the user level is enabled by “wiring” the user level threads with kernel level threads, which in turn are wired to hypervisor-level threads, which in turn are wired to hardware threads. Hardware threads are where the action moves from the abstract to reality. Each core has at least one hardware thread.

## Slide 7: Multithreading in Hardware: Examples
Intel Hyperthreading (Intel HT)
  2 threads per core
AMD Simultaneous multithreading (SMT)
  2 threads per core
IBM Power 9
  4 threads per core
Apple M series
  1 thread per core (to the best of my knowledge)

## Slide 8: Pipelining
Consider addition of two floating point numbers:
Mantissa
Exponent
Mantissa
Exponent
.10101101101111 1001010
.10101111111111 0001010
Shift the mantissa of the smaller number to align the exponents
Add the two mantissa quantities
Normalize the number
Notes: What we think of as a simple operation in a programming language is broken into several to many hardware instructions. It is important for performance and correctness that programmers understand the implication of their code on the hardware. For example, floating point division is notoriously difficult to implement with good performance, yielding reduced performance. Additionally, the imprecision of the floating point operations can yield algorithm instability. There is a tradeoff of course between code readability and maintenance and performance. For example, the use of double precision divisions may be the most straightforward interpretation of a numerical algorithm (e.g. LU factorization). Also, structuring code as small functions and object oriented programming yield better code quality, but they have detrimental impact on the pipeline (branch hazards), and also on the cache and TLB. When in doubt, consider that programmer’s time is far more precious than machine time!

## Slide 9: Tradeoffs
Implementing an instruction without pipelining will be very slow, forcing the frequency of the processor to be very low or will require variable machine cycles to implement instructions
  Throughput will be low
Break the instruction into pieces and implement them on the pipeline. In the previous example, the three micro-ops will be broken further using resources in the execution unit:
  Load the numbers into registers
  Use the shifter to align the first mantissa
  Use the adder to add the two mantissa
  Use the carry bit to adjust the exponent
  Use the sign bit to adjust values
  Use the shifter to normalize
  Store the result
Pipelining allows instructions to overlap in the processor
Improves throughput (BUT not latency or response time)
This is called instruction-level parallelism
Notes: The main idea behind pipelining is to simplify the hardware design and extract instruction-level parallelism. When introduced in the 1960’s, it was held as a panacea for performance. The poor technology at the time did not allow for sophisticated pipelines so the holy grail of “instruction-level parallelism” was left untapped. In the 1980’s the advances in technology yielding faster processor and more components revived the quest for instruction-level parallelism, and we entered the golden age of the compiler, where it was thought that new algorithmic advances in compiler technology would make instruction-level parallelism more visible to the processor. The Alpha processor chip from DEC was hailed as revolutionary at the time as its design was coupled with the compiler, while IBM invented the RISC principle in 1976 to enable faster and simpler pipelines, also benefitting from their compiler technology. UC Berkeley and Stanford later reinvented the RISC principle in the MIPS processor and again they counted on a good compiler to provide performance. In retrospect, instruction-level parallelism was very difficult to extract, yielding complex architectures and IPC was hardly able to cope with the memory wall. The promise ended up being an illusion. In the 1990’s a vigorous debate ensued about the tradeoff: Simplify the pipeline and forget about instruction level parallelism, and count on a higher frequency to build faster pipelines for performance. Or, continue out of order superscalar design with complex pipelines to extract even more instruction level parallelism from the dwindling well. The first camp appeared to be winning for a while with the GigaHertz processor from IBM breaking the GHz frequency barrier. However, the power consumption issues of faster pipeline by 2003 made the speed demon approach impractical, and since then, superscalar processors are the way all processors are designed save for the very low-end embedded processors where cost rather than performance is critical. Hardware designers continue to do work to get incremental improvements for IPC, but the performance quest was largely thrown over the wall to the software programmers, who are expected to write parallel programs. This transition is underway, with multithreading, multicore, and GPU’s providing more and more opportunities for programmers to write parallel code. Unfortunately, like the compiler promises of the 1980’s came to bust, the grand transformation to parallel programs have not materialized into superior performance except in limited (though important) applications in high performance computing, crypto currencies and artificial intelligence (the latter two being the main beneficiaries of GPU’s).

## Slide 10
Loader
Execution Units
(Pipelined)
State
Instruction Cache
Instruction Decode & Op Issue
Load/Store Unit
Memory (Caches, memory controller, bus interface)
I/O
Non Pipelined Picture of a Processor
Notes: These are the building blocks of a modern processor. Nowadays, processor chips are said to be multi-core, which means that there are multiple CPU’s on the chip. Each core has the conceptual picture of the above figure. Chip designers since 2003 have been translating the technology advances in lithography into more cores per chip. This adds more processing power, but strains the memory bandwidth. Additionally, a programmer today is faced with stagnant single thread performance, and the only way to get more performance is to write parallel programs.

## Slide 11
IF
Instruction Cache
ID
L/S
I/O
Pipelined Picture of a Processor
Reg
EX
Memory (Caches, memory controller, bus interface)
IF: Instruction fetch
ID: Instruction decode & issue
Reg: Register file and other state
EX: Execution unit (ALU, FPU, …)
L/S: Load store unit
IF
ID
Reg
EX
L/S
Reg
Notes: The cartoon shows the units in the processor rearranged in a 6-stage simple pipeline (unrealistic, most pipelines in real life are deeper). Note that we insert the yellow boxes that represent registers (or clocked latches) between the stages to hold the intermediate results. Within each stage, the logic takes the input and when the circuits stabilize, they produce an output into the latch of the next stage. A clock signal serves to load the input of the latch and starts the next cycle. Note that the registers introduces additional delay, so an instruction will take slightly longer to execute on a pipelined version than a non-pipelined one. Pipelining is not for latency, it is for throughput. The CPU cycle now has to cover the longest pipeline stage, and thus this is how it is now defined. Note that if we had an FPU, for example, it will be a much longer pipeline. A pipelined division, for example, could run easily in the tens of stages. Divisions are bad for CPU’s!!!

## Slide 12: Observations
This is a 6-stage pipeline
If working to the fullest, it should be running 6 instructions in parallel compared to non-pipelined version
  6x performance increase to instruction-level parallelism (ILP)
Don’t get too excited:
  Not all instructions use all pipeline stages
  If L/S has a cache miss, the pipeline must stall (no more instructions issued)
  Must preserve semantics, and instructions may depend on one another
Notes: In practice, a factor of 2 improvement in throughput is a reasonable target to shoot for an expect.
How far can I pipeline? Can I go all the way to a ridiculous number? We cannot. There is a clock skew that could throw a deep pipeline out of sync. A deep pipeline is limited in its depth by the maximum clock skew in the system.

## Slide 13: Pipeline Bubbles
Structural
Data
Control
L1: ld r1, (r4) # a[i]
L2: ld r2, (r5) # b[i]
L3: fmul r3, r1, r2 # a x b
L4: st r3, (r6) # c[i]
L5: add r4, 8
L6: add r5, 8
L7: add r6, 8
L8: add r0, -1 # I
L9: bne L1
IF
ID
Reg
EX
L/S
Reg
Notes: Ideally, all pipeline stages should be full and every instruction should finish exactly after 6 cycles (in the example given, replace 6 with the number of stages in the pipeline). This ideal is seldom realized in practice, ILP has severe limitations.

## Slide 14: Structure Induced Bubble
L1: ld r1, (r4) # a[i]
L2: ld r2, (r5) # b[i]
L3: fmul r3, r1, r2 # a x b
L4: st r3, (r6) # c[i]
L5: add r4, 8
L6: add r5, 8
L7: add r6, 8
L8: add r0, -1 # I
L9: bne L1
IF
ID
Reg
EX
L/S
Reg
L1, L2 & L4 do not use EX
L3, L5, L6, L7, L8 & L9 don’t use L/S
Register file must support 2 read ops and
1 write op simultaneously
Notes: Not every instruction will use all the pipeline stages. A ld r1, (r4) for example will not use the ALU. The structure of the pipeline will have to introduce a bubble in the ALU for this instruction. This is an example of a structural problem that introduces a bubble.

## Slide 15: Instruction Dependencies (Hazards)
L1: ld r1, (r4) # a[i]
L2: ld r2, (r5) # b[i]
L3: fmul r3, r1, r2 # a x b
L4: st r3, (r6) # c[i]
L5: add r4, 8
L6: add r5, 8
L7: add r6, 8
L8: add r0, -1 # I
L9: bne L1
IF
ID
Reg
EX
L/S
Reg
Read-Write:
L1  L5
L2  L6
L7  L4
Write-Read:
L1, L2  L3
L3  L4
L8  L9
Write-Write:
Not shown here
Notes: Note the data dependencies here: L3 depends on L1 and L2. L4 depends on L3 and L5 through L7 cannot run until L1, L2 and L4 execute, respectively.
The control issue here is that we do not know what to do at L9.

## Slide 16: Control-Induced Bubbles
L1: ld r1, (r4) # a[i]
L2: ld r2, (r5) # b[i]
L3: fmul r3, r1, r2 # a x b
L4: st r3, (r6) # c[i]
L5: add r4, 8
L6: add r5, 8
L7: add r6, 8
L8: add r0, -1 # I
L9: bne L1
IF
ID
Reg
EX
L/S
Reg
Which one is next? L1 or L10???
Notes: Theoretically, we have to wait until L9 computes to be able to decide which is the next instruction to fetch. This will not be decided until the 4th stage in the pipeline and the program counter itself stored elsewhere. This can stall the pipeline for 4 instructions at minimum.

## Slide 17
Pipelines in Action

## Slide 18: Non-Pipelined
L1: ld r1, (r4) # a[i]
L2: ld r2, (r5) # b[i]
L3: fmul r3, r1, r2 # a x b
L4: st r3, (r6) # c[i]
L5: add r4, 8
L6: add r5, 8
L7: add r6, 8
L8: add r0, -1 # I
L9: bne L1
IF | ID | REG | ALU | MEM | REG
L1 | L1 | L1,r4 |  | L1, (r4) | L1, r1
L2 | L2 | L2, r5 |  | L2, (r5) | L2, r2
L3 | L3 | L3, r1 | L3, mul |  | L3, r2
L4 | L4 | L4, r3, L4, r6 |  | L4, (r6) | 
L5 | L5 | L5, r4 | L5, add |  | L5,r4
L6 | L6 | L6, r5 | L6, add |  | L6,r5
L7 | L7 | L7, r6 | L7, add |  | L7,r6
L8 | L8 | L8, r0 | L8, add |  | L8,r0
L9 | L9 | L9,r0 | L9, bne |  | L9, PC
Beware: The cycle here is 6 times the cycle of the pipelined version (next slide).
Notes: The best thing to read this chart is to make an empty table and try to fill it using the code on the left step by step. It is tedious work but will give you a better idea of how the pipeline works. Observe here how these “simplified” RISC instructions are translated into hardware operations of various lengths (and taking different latencies to execute). It is an interesting reflection on the RISC promise of “simple, uniform instructions that make it easy for the compiler to generate code” of the 1970 and 1980 promises. While the RISC vs. CISC debate is now settled, the reality is that modern RISC processors have a lot of CISCiness in them.

## Slide 19: Pipeline Op
L1: ld r1, (r4) # a[i]
L2: ld r2, (r5) # b[i]
L3: fmul r3, r1, r2 # a x b
L4: st r3, (r6) # c[i]
L5: add r4, 8
L6: add r5, 8
L7: add r6, 8
L8: add r0, -1 # I
L9: bne L1
IF | ID | REG | ALU | MEM | REG
L1 |  |  |  |  | 
L2 | L1 |  |  |  | 
L3 | L2 | L1,r4 |  |  | 
L4 | L3 | L2, r5 | L1 |  | 
L4 | L3 |  | L2 | L1 | 
L4 | L3 |  |  | L2 | L1, r1
L4 | L3 |  |  |  | L2, r2
L5 | L4 | L3, r1,r2 |  |  | 
L5 | L4 |  | L3, mul |  | 
L5 | L4 |  |  | L3 | 
L5 | L4 |  |  |  | L3, r3
L6 | L5 | L4, r3, r6 |  |  | 
L7 | L6 | L5, r4 | L4 |  | 
L8 | L7 | L6, r5 | L5, add | L4 | 
L9 | L8 | L7, r6 | L6, add | L5 | 
 | L9 | L8, r0 | L7, add | L6 | L5,r4
 | L9 |  | L8, add | L7 | L6, r5
 | L9 |  |  | L8 | L7, r6
 | L9 |  |  |  | L8, r0
 |  | L9,r0 |  |  | 
 |  |  | L9, bne |  | 
IF
ID
Reg
EX
L/S
Reg
9 instructions in 21 cycles
IPC = 9/21 = 3/7 
Speedup: 3/7 x 6 = 2.57
Notes: Pipeline bypass and data forwarding: It is possible that when an instruction has no use for a certain stage, the control and data are simply “forwarded” to the next stage (if possible) instead of just doing an “no operation” at that stage. Modern pipeline design has no notion of the linear progression that is depicted in the figure. Rather, the pipeline is a set of stations and data are routed between the stations according to the stored program logic.

## Slide 20: Superscalar (Multi-Issue) Pipeline
Instead of issuing one instruction at a time, we issue 2 or 4
Hope is to maximize the exploitation of ILP
Add more resources to the pipeline (another ALU, more ports to the register file, more L/S units, etc.)
Still, preserve the order of execution
The idea is to exploit the independence among the instructions in a single stream and run instructions in parallel when possible.
Notes: Keep in mind that we still do not execute instructions out of order, this comes later. Multi-issue (or superscalar) designs were hailed by the computer architecture research community as the panacea to finally exploit instruction level parallelism. The wild dreams of the 80’s though did not materialize, and instruction level parallelism remains a resource-heavy design methodology with subpar return on the investment.

## Slide 21
IF
Instruction Cache
ID
L/S
I/O
Pipelined Picture of a Processor
Reg
EX
Memory (Caches, memory controller, bus interface)
IF: Instruction fetch
ID: Instruction decode & issue
Reg: Register file and other state
EX: Execution unit (ALU, FPU, …)
L/S: Load store unit
IF
ID
Reg
EX
L/S
Reg
EX
L/S
Add more ports to
the register file, allowing
up to 4 reads and 2 writes
Notes: We expand the pipeline in this example by adding two execution units, two load-store units, and increase the register file to have 4 input ports and 2 output ports

## Slide 22: Multi-Issue Op
L1: ld r1, (r4) # a[i]
L2: ld r2, (r5) # b[i]
L3: fmul r3, r1, r2 # a x b
L4: st r3, (r6) # c[i]
L5: add r4, 8
L6: add r5, 8
L7: add r6, 8
L8: add r0, -1 # I
L9: bne L1
IF | ID | REG | ALU | MEM | REG
L1, L2 |  |  |  |  | 
L3, L4 | L1, L2 |  |  |  | 
L5, L6 | L3, L4 | L1,r4; L2, r5 |  |  | 
L5, L6 | L3, L4 |  | L1, L2 |  | 
L5, L6 | L3, L4 |  |  | L1, L2 | 
L5, L6 | L3, L4 |  |  |  | L1, r1; L2, r2
L6, L7 | L4, L5 | L3, r1,r2 |  |  | 
L6, L7 | L4, L5 |  | L3, mul |  | 
L6, L7 | L4, L5 |  |  | L3 | 
L6, L7 | L4, L5 |  |  |  | L3, r3
L8, L9 | L6, L7 | L4, r3, r6; L5, r4 |  |  | 
 | L8, L9 | L6, r5; L7, r6 | L4; L5, add |  | 
 | L9 | L8, r0 | L6, add; L7 add | L4; L5 | 
 | L9 |  | L8, add | L6, L7 | L5,r4
 | L9 |  |  | L8 | L6, r5; L7, r6
 | L9 |  |  |  | L8, r0
 |  | L9,r0 |  |  | 
 |  |  | L9, bne |  | 
IF
ID
Reg
EX
(2)
L/S
(2)
Reg
9 instructions in 18 cycles
IPC = 9/18 = 0.50 
Speedup: 0.50 x 6 = 3

## Slide 23: One-Step Further: Out of order execution
Issue instructions whenever they are ready to execute, even if not in the right order, as long as the semantics
of the program are not violated

## Slide 24: Out of Order Op
L1: ld r1, (r4) # a[i]
L2: ld r2, (r5) # b[i]
L3: fmul r3, r1, r2 # a x b
L4: st r3, (r6) # c[i]
L5: add r4, 8
L6: add r5, 8
L7: add r6, 8
L8: add r0, -1 # I
L9: bne L1
IF | ID | REG | ALU | MEM | REG
L1, L2 |  |  |  |  | 
L3, L4 | L1, L2 |  |  |  | 
L5, L6 | L3, L4 | L1,r4; L2, r5 |  |  | 
L7, L8 | L5, L6 |  | L1, L2 |  | 
L9 | L7, L8 | L5, r4; L6, r5 |  | L1, L2 | 
 | L9 | L8, r0 | L5, add; L6 add |  | L1, r1; L2, r2
 |  | L3, r1,r2 | L8, add | L5, L6 | 
 |  |  | L3, mul | L8 | L5, r4; L6, r5
 |  |  |  | L3 | L8, r0
 |  | L9, r0 |  |  | L3, r3
 |  | L4, r3, r6; | L9, bne |  | 
L1, L2 |  | L7, r6 | L4; |  | 
L3, L4 | L1, L2 |  | L7, add | L4; | 
L5, L6 | L3, L4 | L1,r4; L2, r5 |  | L7 | 
L7, L8 | L5, L6 |  | L1, L2 |  | L7, r6
9N instructions in 11N+4 cycles
IPC = (9N)/(11N+4) ~ 0.81
Speedup: 0.81 x 6 = 4.86
Observe: We eliminated 3 cycles from the first loop, but the control
hazard is also ameliorated, notice our the first 4 cycles of the next
iteration of the loop are overlapping with the first loop!
IF
ID
Reg
EX
(2)
L/S
(2)
Reg

## Slide 25: One-Step Further: Register Renaming
Superscalar: The idea is to exploit the independence among the instructions in a single stream and run instructions in parallel
when possible. This requires adding resources to the processor, and issuing multiple instructions in a given cycle
Superscalar with out of order: Issue instructions whenever they are ready to execute, even if not in the right order
Superscalar opens the door for parallelism to be exploited. But the dependence among instructions kills parallelism.
Dependence is often based on r-w, w-r, etc. And often the limited number of registers makes the code full of faux
dependences
Solution: Let us rename the registers on the fly to improve parallelism

## Slide 26: Reg Renaming
L1: ld r1, (r4) # a[i]
L2: ld r2, (r5) # b[i]
L3: fmul r3, r1, r2 # a x b
L4: st r3, (r6) # c[i]
L5: add r4, 8
L6: add r5, 8
L7: add r6, 8
L8: add r0, -1 # I
L9: bne L1
IF | ID | REG | ALU | MEM | REG
L1, L2 |  |  |  |  | 
L3, L4 | L1, L2 |  |  |  | 
L5, L6 | L3, L4 | L1,r4; L2, r5 |  |  | 
L7, L8 | L5, L6 |  | L1, L2 |  | 
L9 | L7, L8 | L5, r4; L6, r5 |  | L1, L2 | 
 | L9 | L8, r0, L7, r6 | L5, add; L6 add |  | L1, r1; L2, r2
 |  | L3, r1,r2 | L8, add, L7 add | L5, L6 | 
 |  |  | L3, mul | L7, L8 | L5, r4; L6, r5
 |  |  |  | L3 | L8, r0, L7, r26
 |  | L9, r0 |  |  | L3, r3
 |  | L4, r3, r6; | L9, bne |  | 
L1, L2 |  |  | L4; |  | 
L3, L4 | L1, L2 |  |  | L4; | 
L5, L6 | L3, L4 | L1,r4; L2, r5 |  |  | 
L7, L8 | L5, L6 |  | L1, L2 |  | 
Speed up is almost the
same, register renaming works
better with larger codes
IF
ID
Reg
EX
(2)
L/S
(2)
Reg

## Slide 27: Out of Order Issues
Interrupts?
Exceptions?
Cache misses?
TLB misses?
Memory writes and reads?
Notes: Interrupts come from the hardware. Exceptions occur as a result of the program misbehavior (e.g., illegal memory access). These events occur in the middle of executing instructions. For interrupts, there are three choices: 1. Stop the fetching new instructions and wait for the pipeline to drain. 2. Save the state of the micro architecture in memory to be resumed later (with the help of the OS). 3. Flush all uncommitted instructions. The first is the simplest to implement. The second used to be implemented in old mainframe systems, but not in modern processors. The third option is complex to implement, but as we see, it is necessary in the case of exceptions. For the case of exceptions, there really is one option: The code must stop at the instruction that caused the exception, and all instructions prior to the logical place where the exception occurred must be committed, and all instructions that are partially completed or are tentatively completed (in the case of out of order execution) must be flushed. As you see then, the notions of committing and flushing instructions is central to the pipeline operation. It is often that interrupt handling is piggybacked on top of the exception handling and flushing the pipeline is the option that is used.
And for all the promises of instruction-level parallelism and the complexity and expense of building sophisticated pipelines, a single cache or TLB miss can bring the mightiest pipeline to its knees. Bad memory behavior will cause pipeline stalls with often a 100+ cycle wait for the data to be read (write misses can always be bypassed). Hardware multithreading can mitigate some of these effects, but it does not come for free.

## Slide 28: Compiler Support & Software Implications
The compiler may add support for instruction scheduling:
  Inserting NOP to reduce hazards
  Delayed branch instructions
  Delayed load instructions
Programmers beware!
  Complex operations can challenge the pipeline
  Lack of locality in data references
  Conditional branches
Somewhat fallen out of favor

## Slide 29: An Idea that Works: Loop Unrolling
for(i = 0; i < n; i++)
c[i] = a[i] x b[i];
for(i = 0; i < n; i += 4)
c[i] = a[i] x b[i];
c[i+1] = a[i+1] x b[i+1];
c[i+2] = a[i+2] x b[i+2];
c[i+3] = a[i+3] x b[i+3];
Notes: Loop unrolling came to the fore in the early 80’s. The idea is not simply to reduce the number of tests per loop, but to allow sufficient amounts of straight line code to be scheduled by the pipeline. It exposes from instruction level parallelism. This can be done by a programmer or a compiler. Never do this as a programmer! It will make your code look like a nightmare. A good optimizing compiler can do this for you without too much hassle.

## Slide 30: Loop Unrolling in Action
L1: ld r1, (r4) # a[i]
L2: ld r2, (r5) # b[i]
L3: fmul r3, r1, r2 # a x b
L4: st r3, (r6) # c[i]
L5: add r4, 8
L6: add r5, 8
L7: add r6, 8
L8: add r0, -1 # I
L9: bne L1
L1: ld r1, (r4) # a[i]
L2: ld r2, (r5) # b[i]
L3: fmul r3, r1, r2 # a x b
L4: st r3, (r6) # c[i]
L5: add r4, 8
L6: add r5, 8
L7: add r6, 8
L8: ld r7, (r9) # a[i+ 1 ]
L9: ld r8, (r10) # b[i+ 1 ]
L10: fmul r11, r7, r8 # a x b
L11: st r11, (r12) # c[i+1]
…
L29: add r0, -4 # I
L30: bne L1
Notes: Please keep in mind that loop unrolling increases the code size, which puts some pressure on the instruction cache. If used sensibly, the increase is manageable and the resulting pressure on the cache and memory bandwidth could be minimal (depending on the number of iterations in a loop). For loop with a small number of iterations, the benefits of loop unrolling is reduced.

## Slide 31: Loop Unrolling
L1: ld r1, (r4) # a[i]
L2: ld r2, (r5) # b[i]
L3: fmul r3, r1, r2 # a x b
L4: st r3, (r6) # c[i]
L5: add r4, 8
L6: add r5, 8
L7: add r6, 8
L8: ld r1, (r4) # a[i+ 1 ]
L9: ld r2, (r5) # b[i+ 1 ]
L10: fmul r3, r1, r2 # a x b
L11: st r3, (r6) # c[i+1]
…
L29: add r0, -4 # I
L30: bne L1
IF | ID | REG | ALU | MEM | REG
L1, L2 |  |  |  |  | 
L3, L4 | L1, L2 |  |  |  | 
L5, L6 | L3, L4 | L1,r4; L2,r5 |  |  | 
L7, L8 | L5, L6 |  | L1,r4; L2,r5 |  | 
L9, L10 | L7, L8 | L5, r4; L6, r5 |  | L1,r4; L2,r5 | 
L11, L12 | L9, L10 | L8, L7,r6 | L5, add; L6 add |  | L1,r4; L2,r5
L13, L14 | L11, L12 | L3, r1,r2 | L7 add, L8 | L5, L6 | 
L15, L16 | L13, L14 | L9,r5 | L3, mul | L7 | L5, r4; L6, r5
L17, L18 | L15, L16 |  | L9 | L3 | L7, r26
L19, L20 | L17, L18 |  |  | L8, r4,L9 r5 | L3,r3
L21, L22 | L19, L20 | L4, r3, r6; |  |  | L8, r1,L9,r2
L23, L24 | L21, L22 | L10,r1,r2 | L4; |  | 
L25, L26 | L23, L24 |  | L10,mul | L4; | 
L27, L28 | L25, L26 |  |  | L10 | L4
L29, L30 | L27, L28 |  |  |  | L10,r6
 |  | L11, r3, r6; |  |  | 
IF
ID
Reg
EX
(2)
L/S
(2)
Reg
L8 依赖L5