## Slide 1: Memory Architecture
L2 Cache
L1
L1
L1
L1
L2 Cache
L1
L1
L1
Memory
L1
L1
L1d
L1
L1i
core
Bus
。。。
Notes: The broadcast bus is the simplest form of connections. The earliest shared memory multiprocessors that kept the memory consistent among processors were all implemented on a broadcast bus technology. All participants got to listen to all transactions, which simplified implementations of cache protocols for instance. It also allowed synchronization by locking the bus, in addition to enabling processors to talk to more than one entity at a time. Buses do not have the complication of more sophisticated structures that require complex routing. The problem of the bus structure is both in performance and in physics. In performance, the bus bandwidth is shared among all participants, which means each one of them gets a decreasing share as we add more participants on the bus. In physics, there is only so much length that a bus can have before signal attenuation will make it impractical to operate. This limts the scalability of the bus structure to a typically a handful of processors, certainly no more than a dozen if good performance is to be obtained.